## Slide 1: VOID-NAV
PROBLEM STATEMENT 8 · NEXT GEN COMMUNICATION
Off-grid, multi-hop emergency messaging that keeps working when towers, power and Internet don't
SOS in → hop · hop · hop → delivered ✓ → confirmation back to sender
Notes: VOID-NAV: an infrastructure-independent emergency messaging network built on store-carry-forward multi-hop relaying with end-to-end delivery confirmation.

## Slide 2: When the grid goes dark, so does the call for help
0
cell towers reachable
Backhaul and power loss take base stations down within hours of a major disaster
0
bars of Internet
No cloud, no messaging apps, no location sharing for affected communities
?
did it arrive?
Even when a message escapes, senders and responders can't tell if it reached anyone
Challenge: maintain communication, relay across changing connectivity and thin bandwidth, and give users and responders dependable delivery status.

## Slide 3: VOID-NAV turns every device into a relay
📱
Any device is a node
Phones (BLE / Wi-Fi Direct), LoRa beacons and responder radios form an ad-hoc mesh — no towers, no SIM.
📦
Store · carry · forward
Messages wait in a node's buffer and ride people and vehicles across gaps in the network.
🚨
SOS first
Priority classes set copy budget, TTL and queue order; SOS pre-empts info traffic on thin links.
✅
Delivered receipts
Destination emits a tiny ACK that floods back, confirms to the sender, and purges stale copies.

## Slide 4: Layered architecture, infrastructure-free end to end
Emergency App
SOS button · templates · GPS tag · status ticks
Bundle Layer
Signed message bundles · priority · TTL · custody
Routing Engine
Spray quota + delivery-predictability (PRoPHET) handoff
ACK / Status Plane
Delivery receipts gossiped back · copy purge
Radio Abstraction
BLE · Wi-Fi Direct · LoRa 868/915 MHz · solar relays
Node types
Civilian phones
mobile, intermittent
Responder radios
mobile, long range
Solar relay beacons
static, always-on
Command post gateway
satellite uplink when available

## Slide 5: Life of an SOS: multi-hop out, receipt back
1
Create
Victim taps SOS; bundle gets ID, GPS, priority 0, 16-copy quota
2
Spray
Copies halve at each encounter, fanning out across the crowd
3
Carry
In blackout zones, carriers hold custody until they walk out of the gap
4
Hand-off
Last copy moves only to nodes likelier to meet the destination
5
Deliver
Rescue post receives; duplicate copies are suppressed
6
Confirm
ACK floods back; sender sees ✓✓ delivered and buffers purge
⏳ Queued
↗ Relayed (n hops)
✓ Delivered
✓✓ Confirmed to sender

## Slide 6: Routing tuned for scarce, broken links
Priority | Copy quota | TTL | Buffer policy
P0 · SOS | 16 | 100 min | Never evicted; may evict P1/P2
P1 · Urgent | 8 | 67 min | Evicts P2 when full
P2 · Info | 4 | 42 min | First to drop
Delivery predictability
On meeting b:
P(a,b) ← P + (1−P)·0.75
Transitive:
P(a,c) ← max(P, P(a,b)·P(b,c)·0.25)
Aging per 10 s:
P ← P·0.995
Hand off last copy only if P(b,dst) > P(a,dst) + 0.05
Bandwidth cap of 4 bundles per contact per 10 s is spent in priority order — an SOS never waits behind a status update.
ACK digests are a few bytes of message IDs, merged on every contact where the two sets differ.

## Slide 7: Evaluation under simulated network outages
66
nodes (60 mobile, 6 static relays)
1 km²
disaster zone, 120 m radio range
100 min
simulated, 10 s steps
120
messages / run, 20% SOS
0–50%
nodes killed at t = 20 min
5
seeds per point, 4 protocols
Plus a regional blackout: every node in the western 40% of the zone goes silent from minute 33 to 50 — modelling a power-cut sector.

## Slide 8: Delivery holds up as the network falls apart
Chart: Delivery ratio (%) vs. nodes failed
| 0% | 10% | 20% | 30% | 40% | 50%
Direct carry | 94 | 85 | 70.6 | 62.2 | 53.3 | 44.5
Epidemic flood | 99 | 94.2 | 85.2 | 82.5 | 78.8 | 73.2
Spray & Wait | 100 | 94.4 | 85.7 | 80.8 | 75.1 | 68.2
VOID-NAV | 99.2 | 94.6 | 85.7 | 80.1 | 74.9 | 67.9
68%
of messages still delivered with half the network destroyed
+23 pts
over direct carrying at 50% failure; within 5 pts of flooding

## Slide 9: SOS messages arrive twice as fast as spray-and-wait
Chart: Median SOS latency at 20% failure (minutes)
| Direct carry | Epidemic flood | Spray & Wait | VOID-NAV
Median SOS latency (min) | 13.8 | 1.8 | 4.4 | 2.4
Chart: Cumulative % of all messages delivered by time
| 0m | 2m | 4m | 6m | 8m | 10m | 15m | 20m | 30m | 45m | 60m
Direct carry | 4.4 | 10.2 | 14.9 | 21 | 26.6 | 31.8 | 39.2 | 45.4 | 55 | 64.5 | 68.7
Epidemic flood | 8.7 | 49.2 | 62.3 | 66.5 | 71.7 | 73.8 | 78.5 | 80.4 | 83.5 | 84.8 | 85.2
Spray & Wait | 7.9 | 25.1 | 40.5 | 53.1 | 64.5 | 70.8 | 79.3 | 82.8 | 85.5 | 85.7 | 85.7
VOID-NAV | 8.3 | 30.1 | 45.3 | 54.2 | 63.1 | 67.9 | 77 | 81.8 | 85.1 | 85.7 | 85.7

## Slide 10: Flooding works, but burns scarce bandwidth
Chart: Data transmissions per delivered message (20% failure)
| Epidemic flood | Spray & Wait | VOID-NAV
Transmissions per delivered message | 710.3 | 14.1 | 17.7
40×
less data traffic than epidemic flooding at near-identical delivery
Fewer transmissions mean longer phone batteries, less radio contention, and room for SOS traffic on LoRa duty-cycle limits. Receipts add ~35 tiny digest exchanges per delivery.

## Slide 11: Senders know their message got through
Chart: Delivered messages confirmed back to sender (%), by nodes failed
| 0% | 10% | 20% | 30% | 40% | 50%
Delivered messages confirmed to sender (%) | 100 | 99.2 | 97.4 | 97.1 | 96.4 | 94.6
97%
receipts returned at 20% failure
4.3 min
median send → ✓✓ confirmation
0
baselines that give any delivery status

## Slide 12: Resilience scorecard at 30% node failure
Protocol | Delivery | SOS delivery | SOS latency | Tx / delivery | Delivery receipts
Direct carry | 62.2% | 65.1% | 13.6 min | 1.0 | —
Epidemic flood | 82.5% | 87.9% | 1.7 min | 631.2 | —
Spray & Wait | 80.8% | 84.7% | 3.8 min | 14.3 | —
VOID-NAV | 80.1% | 84.8% | 3.0 min | 18.3 | 97%
Only VOID-NAV combines flood-class delivery, fast SOS, low overhead and end-to-end confirmation.

## Slide 13: Demonstration and roadmap
Run it yourself
python3 sim/voidnav.py results/results.json
Pure Python, no dependencies, seeded and reproducible
Sweeps 4 protocols × 6 outage levels × 5 seeds
Emits JSON that rebuilds every chart in this deck
Now
Simulator, routing engine, ACK plane, evaluation
Next
Android app over BLE + Wi-Fi Direct; LoRa relay firmware
Then
Field trial with responders; end-to-end encryption and signed bundles

## Slide 14: No towers. No Internet. Still heard.
VOID-NAV · multi-hop · priority-aware · delivery-confirmed